## Instructions. Development of Real-Time Systems – Assignment 3

Overview
In this assignment we will focus a bit more on the theoretical side. We will have a look at verifying real-time system by using the cyclic structured construct handled in the course and a simulation environment to automatically schedule a full timeline. The main purpose of the assignment is to expose the student to several ways of planning and verifying a real-time system in practice.
Theory assignment.
The following part of assignment is a purely theoretical task that requires no additional tools. The task is to find the largest possible frame size for the cyclic structured scheduler by following requirements 1,2 and 3 for finding the largest frame size. The following three task sets should be used:
Based on week 2 : Cyclic Structured Scheduling
Ti(Pi, ei, Di) pi = period, ei = execution time, Di = Relative deadline
1. T1(15, 1, 14)
2. T2(20, 2, 26)
3. T3(22, 3)
If there is not deadline, we consider deadline the new time the task will appears. That is to say the period.

  - f ≥ max(e1,e2,...,en) f → f >= 3
  - ∃i: mod(pi,f)= 0 f E {22, 20, 15, 11, 10, 5, 4, 3, 2, 1} → All the divisors of the period can be a feasible candidate.
  - 2*f – gcd(pi,f) ≤ Di for i= 1, 2, ..., n
f	T1	T2	T3
22	2 * 22 – gcd(15, 22) = 44 – 1 = 43 ≤ 14 No
20	2 * 20 – gcd(15, 20) = 40 – 5 = 35 ≤ 14 No
15	2 * 15 – gcd(15, 15) = 40 – 15 = 25 ≤ 14 No
10	2 * 10 – gcd(15, 10) = 20 – 5 = 15 ≤ 14 No
5	2 * 5 – gcd(15, 5) = 10 – 5 = 5 ≤ 14 Yes	2 * 5 – gcd(20, 5) = 10 – 5 = 5 ≤ 26 Yes	2 * 5 – gcd(22, 5) = 10 – 1 ≤ 22 Yes

The optimal framesize is 5.

Ti(Pi, ei, Di) pi = period, ei = execution time, Di = Relative deadline

1. T1(4, 1)
2. T2(5, 2, 7)
3. T3(20, 5)
  - f ≥ max(e1,e2,...,en) f → f >= 5
  - ∃i: mod(pi,f)= 0 f E {20, 10, 5, 4, 2, 1} → All the divisors of the period can be a feasible candidate.
  - 2*f – gcd(pi,f) ≤ Di for i= 1, 2, ..., n
f	T1	T2	T3
20	2 * 20 – gcd(4, 22) = 40 – 1 = 39 ≤ 4 No
10	2 * 10 – gcd(4, 10) = 20 – 2 = 18 ≤ 4 No
5	2 * 5 – gcd(4, 5) = 10 – 1 = 9 ≤ 4 No

It is not feasible to find a period that fulfil the requirements. Job T3 should be splited in smaller parts.

Ti(Pi, ei, Di) pi = period, ei = execution time, Di = Relative deadline

1. T1(5, 0.1)
2. T2(7, 1)
3. T3(12, 6)
4. T4(45, 9)
  - f ≥ max(e1,e2,...,en) f → f >= 9
  - ∃i: mod(pi,f)= 0 f E {45, 15, 12, 9, 7, 6, 5, 3, 2, 1} → All the divisors of the period can be a feasible candidate.
  - 2*f – gcd(pi,f) ≤ Di for i= 1, 2, ..., n

f	T1	T2	T3	T4
45	90 - 5 ≤ 5 No
15	30 - 5 ≤ 5 No
12	24 - 1 ≤ 5 No
9	18 - 1 ≤ 5 No
7	14 - 1 ≤ 5 No
6	12 - 1 ≤ 5 No
5	10 - 5 ≤ 5 Yes	10 – 1 ≤ 7 No
4	8 – 1 ≤ 5 No
3	6 - 1 ≤ 5 Yes	6 – 1 ≤ 7 Yes	6 – 3 ≤ 12 Yes	6 – 3 ≤ 45 Yes

It is not feasible to find a period that fulfil the requirements. Job T3 and T4 should be splited in smaller parts.

Simulation assignment
The assignment is to use a real-time simulator to verify feasibility of a set of tasks. Input the tasks:
Ti(Pi, ei, Di) pi = period, ei = execution time, Di = Relative deadline

1. T1(2, 0.5)
2. T2(3, 1.2),
3. T3(6, 0.5)
and the RM scheduler into the SimSo simulator. Use SimSo to schedule the task set
Provide a report answering the following questions:
What is the utilization factor of the system and what is the value for Urm(3).
U = sum from{i=1 } to{n} {{e_i} over {P_i}} = {0,5} over {2} + {1,2} over {3} + {6} over {0,5} = 0,7333 U_rm(n) = n(2^{1/n} - 1) U_rm(3) = 3(2^{1/3} - 1) = 0,7798

Simulator shows: 0,7410

What is the minimum/maximum/average response time of all tasks?

Is any task missing the deadline? Which task? Where?
There is no task that miss the deadline

Input the tasks:
Ti(Pi, ei, Di) pi = period, ei = execution time, Di = Relative deadline

1. T1(2, 0.5, 1.9)
2. T2(5, 2)
3. T3(1, 0.1, 0.5)
4. T4(10, 5, 20)
  and the EDF scheduler into the SimSo simulator. Use SimSo to schedule the task set.

Provide a report answering the following questions:
What is the utilization factor of the system and what is the value for Urm(4).

The simulator says that the total utilization is 1.

U = sum from{i=1 } to{n} {{e_i} over {P_i}} = {0,5} over {2} + {2} over {5} + {0,1} over {1} + {5} over {10} = 1,25 U_rm(n) = n(2^{1/n} - 1) U_rm(4) = 4(2^{1/4} - 1) = 0,7568

What is the minimum/maximum/average response time of all tasks?

Is any task missing the deadline? Which task? Where?

Task 4 fails at time 30 it exceeds the deadline.
If a deadline is missed, could it be avoided by changing the scheduler?
The main problem here is the utilization is too high to allow the system work properly. Adding a new processor would fix the problem.

ANNEX

References: http://nptel.ac.in/courses/Webcourse-contents/IIT%20Kharagpur/Embedded%20systems/Pdf/Lesson-29.pdf

References : http://www.engr.iupui.edu/~dskim/Classes/ESW5004/RTSys%20Lecture%20Note%20-%20ch04%20Clock-Driven%20Scheduling.pdf

Minimum Context Switching:

- This constraint is imposed to minimize the number of context switches occurring during task execution. The simplest interpretation of this constraint is that a task instance must complete running within its assigned frame. Unless a task completes within its allocated frame, the task might have to be suspended and restarted in a later frame. This would require a context switch involving some processing overhead. To avoid unnecessary context switches, the selected frame size should be larger than the execution time of each task, so that when a task starts at a frame boundary it should be able to complete within the same frame. Formally, we can state this constraint as:
  - max({e}) < F where ei is the execution times of the of task Ti , and Fis the frame size. Note that this constraint imposes a lower-bound on frame size, i.e., frame size F must not be smaller than max({ei})
  - To avoid preemption, want jobs to start and complete execution within a single frame: f ≥ max(e1,e2,...,en)

- To minimize the number of entries in the cyclic schedule, the hyper-period should be an integer multiple of the frame size (⇒f divides evenly into the period of at least one task): ∃i: mod(pi,f)= 0
- To allow scheduler to check that jobs complete by their deadline, should be at least one frame boundary between release time of a job and its deadline:
  2*f – gcd(pi,f) ≤ Di for i= 1, 2, ..., n

References: http://britton.disted.camosun.bc.ca/GCD_LCM.htm

Greatest Common Divisor
The greatest common divisor (GCD), which is also known as the greatest common factor (GCF), of two or more integers is the largest integer that is a common divisor (factor) of all the given integers.
The greatest common divisor of two or more integers can be obtained in three steps:
STEP 1: Find the prime factorization of each integer.
375 = 3 × 53
525 = 3 × 52 × 7
STEP 2: List the common prime divisors (factors) with the least power of all the given integers.
375 = 3 × 53 = 3 × 52 × 5
525 = 3 × 52 × 7 = 3 × 52 × 7
Common Prime Divisors (Factors) with Least Power: 3 and 52
STEP 3: Multiply the common prime divisors (factors) to find the greatest common divisor (factor).
3 × 52 = 75
GCD (GCF) of 375 and 525 = 75
Least Common Multiple
The least common multiple (LCM), which is also known as the least common denominator (LCD) in fractions, of two or more integers is the smallest integer that is a common multiple (denominator) of all the given integers.
The least common multiple (denominator) of two or more integers can be obtained in three steps:
STEP 1: Find the prime factorization of each integer.
  4 = 22
10 = 2 × 5
45 = 32 × 5
STEP 2: List the prime divisors (factors) with the greatest power of all the given integers.
  4 = 22
10 = 2 × 5
45 = 32 × 5
Prime Divisors (Factors) with Greatest Power: 22, 32, and 5
STEP 3: Multiply the prime divisors (factors) to find the least common multiple (denominator).
22 × 32 × 5 = 180
LCM of 4, 10 and 45 = 180